Hardware Project #1: OLED Display
# Assembly
First, make sure the Raspberry Pi is not powered. Plug the circuit board into
a Raspberry Pi on pins 1, 3, 5, 7 and 9 (see the picture to the right). WARNING! Incorrectly installing the display could damage both the display and the Raspberry Pi. Please have one of the organisers check that the display is plugged in correctly before applying power.
# Software Setup
Tip: The following commands require root permissions to run. Sudo runs a command with root permissions. Instead of typing sudo before every command, you can type sudo su to enter root mode before entering the commands that require root permissions. Type exit to return to regular permissions.
Before writing data to the display, several software changes need
to be made on the Raspberry Pi. First, a device tree overlay and
parameter need to be setup in /boot/config.txt. The overlay
needed is the ssd1306.dtbo file (this file can be downloaded from
https://sites.google.com/site/mincepi/pi2oled/files). This overlay sets up some parameters for the display, sets up I2C (used to
communicate with the display) and creates a frame buffer for the
display data. Use the following command to copy the overlay file to
the /boot/overlays directory so that it can be used in config.txt.

sudo nano /boot/config.txt

Add the following lines to the bottom of the file:

dtoverlay=ssd1306,inverted,sequential
dtparam=i2c_arm=on,i2c_baudrate=1000000

The first line enables the overlay we copied into /boot/config.txt, while the second line sets up I2C. To exit out of the editor, type Ctrl-X, then type y and finally press Enter. The software setup is now complete. Reboot the Raspberry Pi for the changes to take effect.
Continued overleaf
# Display Control
We need to run some commands before we can output text to the OLED screen. The following command sets the font we want to use for the display:

setfont Lat7-Terminus16
Now we are going to map the display’s frame buffer to the terminal tty8. There are normally seven consoles numbered from tty1 through tty7 on a Raspberry Pi. The first six are used as command-line interfaces (CLIs) and the seventh is used for a graphical user interface (GUI). The following command maps frame buffer number 1 to console number 8 (tty8).

con2fbmap 8 1
Next, enter the following command to activate the tty8 console.

chvt 8
Now we can display text on the OLED screen. The following command will print “Testing 1 2 3...” on the screen. The echo command prints text to a console. The -n flag removes the trailing newline character to prevent the display from scrolling and the -e flag exectutes escape sequences (such as \ec, which resets the screen’s text, or \n, which prints a newline character). The > symbol pipes the output of the command into a file, which in this case is console tty8.
Tip: For more information on a command, type man COMMAND. This opens a page of information about the command and about how to use the command. Use the up and down arrow keys to move through the file and type q to exit. Most commands have a man pages.

echo -n -e “\ecTesting 1 2 3...\n “ > /dev/tty8
The words “Testing 1 2 3…” should appear on the OLED screen. If they do not, notify one of the organisers. For a more interesting example, we can print the Raspberry Pi’s IP address. The following command has the same configuration as the command above, but now with `hostname -I` instead of the “Testing 1 2 3...” text. The command hostname -I prints the IP address of the Raspberry Pi. Note: the symbols before and after hostname -I in the echo command are not single quotes but rather back quotes (the key for the back quote is found in the upper-left corner of the keyboard). The back quotes make echo execute the hostname -I command rather than just printing “hostname -I” to the screen.

echo -n -e "\ec`hostname -I`\n" > /dev/tty8
The IP address of the Raspberry Pi should now appear on the screen. Congratulations! You have completed the OLED screen tutorial.

Bonus: See if you can figure out how to get the display to show the Pi's processor speed and temperature.
Hint: the processor speed is in the file /sys/devices/system/cpu/cpu0/cpufreq/scaling_cur_freq and the command cat prints the contents of a file. The command vcgencmd measure_temp prints the processor temperature.